## Slide 1: Datacenter Networks
CPSC 433/533, Spring 2021 Anurag Khandelwal

## Slide 2: Recap
What is a data center network?
  Scale, service-model, application characteristics
What makes it different?
  Characteristics, goals (w.r.t. internet), degrees of freedom
How do we achieve goals by exploiting freedom?
  Topology redesign, L2/L3 redesign, L4 redesign

## Slide 3: Recap
What is a data center network?
  Scale, service-model, application characteristics
What makes it different?
  Characteristics, goals (w.r.t. internet), degrees of freedom
How do we achieve goals by exploiting freedom?
  Topology redesign, L2/L3 redesign, L4 redesign
  We will look at some approaches, not all

## Slide 4: How do we achieve DCN goals?
Network architecture design [Done]:
  rearchitect network topology to achieve full-bisection b/w
  DC as a giant switch => Clos/fat-tree topologies
L2/L3 design:
  Via modifications to LS/DV + ECMP
  New addressing / routing / forwarding for new topology
L4 design [Today]:
  transport protocol design to meet DCN goals

## Slide 5: How do we achieve DCN goals?
L4 design:
  Transport protocol design (w/ Fat-Tree)
Many slides courtesy of Mohammad Alizadeh, MIT

## Slide 6: What’s “ideal” ?
What is the best measure of performance for a data center transport protocol?
  Latency of each packet in the flow?
  Number of packet drops?
  Link utilization?
  Average queue length at switches?
  When the flow is completely transferred?
What does the application/user care about?

## Slide 7: Flow Completion Time (FCT)
Time from when flow started at the sender, to when all packets in the flow were received at the receiver

## Slide 8: FCT with TCP
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733
TCP-DropTail: TCP with “drop-tail” queues at switches (drops packets at the tail of the queue)

## Slide 9: Recall: “Elephants” and “Mice”
55% of flows
3% of bytes
5% of flows
35% of bytes
<100KB
>10MB
  Microsoft [Alizadeh 2010]
    Web search (north-south), data mining (east-west)

## Slide 10: FCT with TCP
Problem: the mice are delayed by the elephants
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733

## Slide 11: Solution: use priorities! [pFabric, Sigcomm 2013]
Packets carry a single priority number
  priority = remaining flow size (e.g., #bytes un-ACKed)
Switches
  very small queues (e.g., 10 packets)
  send highest priority / drop lowest priority packet
Servers
  Transmit/retransmit aggressively (at full link rate)
  Drop transmission rate only under extreme loss (timeouts)

## Slide 12: FCT
Chart: Load
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8
Ideal | 1.0066 | 1.0018 | 1.0026 | 1.0035 | 1.0051 | 1.0061 | 1.007 | 1.008
pFabric | 1.0192 | 1.0359 | 1.0528 | 1.0707 | 1.0896 | 1.1088 | 1.1279 | 1.1435
TCP-DropTail | 2.7128 | 3.8866 | 5.0537 | 6.5398 | 8.4256 | 11.0812 | 15.0502 | 20.3733

## Slide 13: Why does pFabric work?
Consider problem of scheduling N jobs at a queue
  J1, J2, … , Jn with duration T1, T2, …Tn respectively
How do you minimize average job completion time?
“Shortest Job First” (SJF) scheduling
  Pick job with minimum Ti ; de-queue and run ; repeat
  I.e., job that requires minimum runtime has max priority
Solution for a network of queues is NP-hard
Setting priority = remaining flow size is a heuristic to approximate SJF

## Slide 14: Questions?

## Slide 15: Network Management & Software Defined Networks
Slides thanks to Scott Shenker, one of the pioneers of SDN

## Slide 16: Goal for rest of the discussion
Provide the “why” of software-defined networking
  Deeper understanding of the problem
  An exercise in architectural thinking
  To build a principled approach towards a solution
Only a high level of the “what”
  Enough that some of you will want to know more
  Take advanced networking course or do research!

## Slide 17: What is Network Management?
Recall the two “planes” of networking
Data plane: forwarding packets
  Based on local forwarding state
Control plane: computing that forwarding state
  Involves coordination with rest of system
Broad definition of “network management”:
  Everything having to do with the control plane

## Slide 18: Original goals for the control plane
Basic connectivity: route packets to destination
  Local state computed by routing protocols
  Globally distributed algorithms
Inter-domain policy: find policy-compliant paths
  Done by globally distributed BGP
For long time, these were the only relevant goals!
  What other goals are there in running a network?

## Slide 19: Isolation
L2 broadcast protocols often used for discovery
  Useful but unscalable and invasive
Want multiple logical LANs on a physical network
  Retain usefulness, cope with scaling, provide isolation
Use VLANs (virtual LANs) tags in L2 headers
  Controls where broadcast packets go
  Gives support for logical L2 networks
  Routers connect these logical L2 networks

## Slide 20: Access Control
Operators want to limit access to various hosts
  “Don’t let laptops access backend database machines”
This can be imposed by routers using ACLs
  ACL: Access Control List
Example entry in ACL: <header template; drop>
  If not port 80, drop
  If source address = X, drop

## Slide 21: Traffic Engineering
Want to avoid persistent overloads on links
Choose routes to spread traffic load across links
Example:
  Adjusting weights in OSPF
Done with centralized computation
  Take snapshot of topology and load
  Compute appropriate OSPF state
  Send to network

## Slide 22: Network management has many goals
Achieving these goals is job of the control plane…
…which currently involves many mechanisms
Globally distributed: routing algorithms
Manual/scripted configuration: ACLs, VLANs
Centralized computation: Traffic engineering

## Slide 23: Bottom Line
Many different control plane mechanisms
Each designed from scratch for their intended goal
Encompassing a wide variety of implementations
  Distributed, manual, centralized,…
Network control plane is a complicated mess!

## Slide 24: Questions?

## Slide 25: Making Network Operators Cry: A Two Step Process

## Slide 26: Step 1: Large datacenters
100,000s machines; 10,000s switches
This is pushing the limits of what we can handle...

## Slide 27: Step 2: Multiple tenancy
Large datacenters host many customers
Each customer gets their own logical network
  Customer should be able to set policies on this network
  ACLs, VLANs, etc.
If there are 1000 customers, that adds 3 orders of magnitude
This goes way beyond what we can handle

## Slide 28: Network Operators Are Now Weeping
Ad hoc control for millions of networked entities
  And something goes wrong
  Try debugging that…
What is the key problem here?
  Complexity
We need a simpler, more systematic design
  How do we achieve this?

## Slide 29: An Example Transition: Programming
Machine languages: no abstractions
  Had to deal with low-level details
  Mastering complexity was crucial
Higher-level languages: OS and other abstractions
  File system, virtual memory, abstract data types, ...
Modern languages: even more abstractions
  Object orientation, garbage collection,...
Abstractions key to extracting simplicity

## Slide 30: What About Network Abstractions?
Consider the data and control planes separately
Different tasks, so naturally different abstractions

## Slide 31: Abstractions for Data Plane: Layers
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 32: The Importance of Layering
Decomposed delivery into basic components
Independent, compatible innovation at each layer
  Clean “separation of concerns”
  Leaving each layer to solve a tractable problem
Responsible for the success of the Internet!
  Rich ecosystem of independent innovation
Think about it….
  Original architecture has handled many order-of-magnitude changes in speed, size, scope, diversity

## Slide 33: Control Plane Abstractions
?

## Slide 34: Many Control Plane Mechanisms
Variety of goals, no modularity:
  Routing: distributed routing algorithms
  Isolation: ACLs, VLANs, Firewalls,…
  Traffic engineering: adjusting weights, MPLS,…
Control Plane: mechanism without abstraction
  Too many mechanisms, not enough functionality

## Slide 35: Questions?

## Slide 36: Finding Control Plane Abstractions

## Slide 37: How do you find abstractions?
You first decompose the problem….
…and define abstractions for each sub-problem
So what is the control plane problem?

## Slide 38: Computing forwarding state
Consistent with low-level hardware/software
  Which might depend on vendor
Based on entire network topology
  Because many control decisions depend on topology
For all routers/switches in network
  Every router/switch needs forwarding state

## Slide 39: Our current approach
Design one-off mechanisms that solve all three
Introduces a lot of complexity
  Think back to the DCN operator

## Slide 40: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 41: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 42: Abs#1: Forwarding Abstraction
Express intent independent of implementation
  Don’t want to deal with proprietary HW and SW
OpenFlow is current proposal for forwarding
  Standardized interface to switch
  Configuration in terms of flow entries: <header, action>
Design details concern exact nature of:
  Header matching
  Allowed actions

## Slide 43: Two Important Facets to OpenFlow
Switches accept external control messages
  Not closed, proprietary boxes
Standardized flow entry format
  So switches are interchangable

## Slide 44: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 45: Abs#2: Network State Abstraction
Abstract away various distributed mechanisms
Abstraction: global network view
  Annotated network graph provided through an API
Implementation: “Network Operating System”
  Runs on servers in network (“controllers”)
Information flows both ways
  Information from routers/switches to form “view”
  Configurations to routers/switches to control forwarding

## Slide 46: Network Operating System
Think of it as a centralized link-state algorithm
Switches send connectivity info to controller
Controller computes forwarding state
  Via some control program that uses the topology as input
Controller sends forwarding state to switches
Controller is replicated for resilience
  System is only “logically centralized”

## Slide 47: Software Defined Network (SDN)
Control Program
Network OS
Global Network View
Traditional Control Mechanisms
Network of Switches and/or Routers
Distributed algorithm running between neighbors
Complicated task-specific distributed algorithm
routing, access control, etc.

## Slide 48: Major Change in Paradigm
Control program:
  Network configuration is a function of the global view
Control mechanism now program using NOS API
Not a distributed protocol, just a graph algorithm

## Slide 49: Separate Concerns with Abstractions
Be compatible with low-level hardware/software
  Need an abstraction for general forwarding model
Make decisions based on entire network
  Need an abstraction for network state
Compute configuration of each physical device
  Need an abstraction that simplifies configuration

## Slide 50: Abs#3: Specification Abstraction
Control mechanism expresses desired behavior
  Whether it be isolation, access control, or QoS
It should not be responsible for implementing that behavior on physical network infrastructure
  Requires configuring the forwarding tables in each switch
Proposed abstraction: abstract view of network
  Abstract view models only enough detail to specify goals
  Will depend on task semantics

## Slide 51: Simple Example: Access Control
Global
Network View
Abstract Network
View
A
B
A
B

## Slide 52: Software Defined Network
Network OS
Global Network View
Abstract Network View
Control Program
Virtualization Layer

## Slide 53: Clean Separation of Concerns
Control program: express goals on abstract view
  Driven by Operator Requirements
Virt. Layer: abstract view  global view
  Driven by Specification Abstraction for particular task
NOS: global view  physical switches
  Controller API: driven by Network State Abstraction
  Switch interface: driven by Forwarding Abstraction

## Slide 54: SDN: Layers for the Control Plane
Network OS
Global Network View
Abstract Network View
Control Program
Virtualization Layer

## Slide 55: Access Control Application
Control program decides who can talk to who
Pass this information to SDN platform
Appropriate ACL flow entries are added to network
  In the right places (based on the topology)
The control program that decides who can talk to whom doesn’t care what the network looks like!

## Slide 56: Takeaway
SDN is not a revolutionary technology…
  …just a way of organizing network functionality
But that’s all the Internet architecture is….
  The Internet architecture isn’t clever, but it is deeply wise
  SDN isn’t clever, but hopefully it is wise….

## Slide 57: Future of Networking: A Systems Perspective

## Slide 58: Goals of this Discussion
We have already seen some of the recent directions
  Datacenter networks, with protocol innovations across L2-L5
  Software defined networks, rearchitecting the control plane
The remainder of this discussion:
  How a systems researcher sees the future of networking
Don’t worry, this won’t be on the exam 

## Slide 59
“Skate where the puck's going, not where it's been”
– Walter Gretzky

## Slide 60: So where is the puck going?

## Slide 61: Typical Server Node
RAM
SSD
HDD
CPU
Memory Bus
PCI
SATA
Ethernet

## Slide 62: Typical Server Node: Yearly Improvements
RAM
SSD
HDD
CPU
Memory Bus
PCI
SATA
Ethernet
30%
30%
30-32%
>30%
15%
15-20%
20%
33-40%
So what does this mean?

## Slide 63: Growth Rates
Network b/w growth (33-40% per year) outpacing:
  CPU (30-32%)
  memory bus (15% per year)
  PCIe (15-20% per year)
  SATA (20% per year)
Current speeds:
  Network b/w: 12.5GB/s
  Memory bus: 80GB/s
  PCIe: 16 GB/s
  SATA: 600 MB/s

## Slide 64: A Couple of Implications
Network stack processing will become a bottleneck
  CPU speed growth vs. network speed growth
Accessing SSD locally will be slower than accessing remote memory
  PCIe bus speed growth vs. network speed growth

## Slide 65: Network Stack Processing
Existing OS network stacks designed for 1 Gbps
Example:
  Typical TCP processing: ~3.2 Gbps per core
  With low-level optimizations: ~9-12 Gbps per core
  TCP on a 40 Gbps link: > 3 cores per server
  TCP on a 100 Gbps link: > 8 cores per server
This is not economically sustainable…
  A core used for n/w stack is a core stolen from “useful” processing by applications/customers

## Slide 66: How do we fix this?
Research trend: kernel bypass
  Packet rates: ~90k pkts/s (1 Gbps), ~9M pkts/s (100 Gbps)
  Traversing the kernel stack is too expensive
  Bypass the kernel completely
  Where do the protocol implementations go?
    User-space for lightweight applications, or…
Research trend: hardware offload
  Implement TCP (+other protocols) on specialized h/w
  Lots of interesting challenges

## Slide 67: Remote memory faster than SSDs
Consider 4kB page, 100Gbps link, 1 switch hop
  Zero queueing delay
Baseline: 4.78 us
  OS: 1.9us, Data copy: 2us, Switching: 0.48us, Propagation Delay: 0.08us, Transmission Delay: 0.32us
How can we avoid OS overhead?
  Research Trend: RDMA

## Slide 68: Traditional DMA
RAM
SSD
CPU
Server
DMA Controller
1
CPU issues DMA request
DMA controller copies data from SSD to RAM
Controller interrupts CPU when done
CPU can now access memory
2
3
4
Note: CPU and CPU <-> memory bus are free during DMA

## Slide 69: RDMA
RAM
CPU
Server
1
CPU issues RDMA request
Local NIC sends RDMA request to remote NIC, which performs DMA & sends data back. Local NIC copies data to RAM
Local NIC interrupts CPU when done
CPU can now access memory
2
3
4
RAM
CPU
NIC
Remote Server
Note: CPU and CPU <-> memory bus are free during RDMA (both local & remote)
Note: OS is bypassed on both ends
NIC

## Slide 70: Remote memory faster than SSDs
Consider 4kB page, 100Gbps link, 1 switch hop
  Zero queueing delay
Baseline: 4.78 us
  OS: 1.9us, Data copy: 2us, Switching: 0.48us, Propagation Delay: 0.08us, Transmission Delay: 0.32us
With RDMA: 2.88us
  Can reduce data copy overheads with NIC support
  Brings latency down to 1.88us!
  ~10x of local memory, 1/10x of local SSD

## Slide 71: What are the challenges?
This assumes zero queueing delay…
  Transport protocol design to minimize queueing delay
  Recall pFabric; Other protocols: DCTCP, pHost, …
RDMA requires lossless ethernet
  Via ethernet flow control or priority flow control (PFC)
  Lossless networks: very active area of research

## Slide 72: Taking it one step further: Resource Disaggregation
Disaggregated Computer
  Instead of a network of computers
Benefits?
  Resource utilization, upgradeability, fault-tolerance
Traditional Datacenter
Network fabric
DRAM
CPU
SSD
Server#1
DRAM
CPU
SSD
Server#N
…
CPU
CPU
CPU
DRAM
DRAM
DRAM
SSD
SSD
SSD
TPU
GPU
Datacenter with Resource Disaggregation
Network fabric

## Slide 73: My Current Research Focus
How can we design OS for disaggregated computer?
  Where does the OS logic run?
Idea: Put key OS functionalities in network fabric
  Why?
  Network has all the visibility…
SDN design to modularize & layer OS functionality
  e.g., Address translation = data plane; memory allocation = control plane, etc.
Remind you of something?
  Forwarding = data plane; route computation = control plane

## Slide 74: Questions?